## Slide 1
Alternative Fumigants for Stored Products ….or, Alternatives to Fumigation
Tom Phillips
Department of Entomology
Kansas State University, Manhattan, KS, USA

## Slide 2: Topics Covered Today
IPM for stored grain
Preventive measures
  Aeration
  Residual sprays/grain protectants
Fumigants and alternatives
Summary, questions, discussion

## Slide 3: Stored Product IPM Basics: Prevent, Monitor, Decide: Fumigate, Sell or Hold Steady
Prevention
  Clean bins
  Seal bins (for possible fumigation….)
  Apply residual insecticides to bin and grain
  Store dry grain; aerate to cool grain
Monitor and record temperature, grain quality, and pest presence/numbers
If insect threshold (=comfort level) is surpassed, then fumigate

## Slide 6
No confined space applications
All applications from outside top hatch

## Slide 7
Monitoring Insects by Taking Direct Grain Samples

## Slide 8: Grain Probe Traps

## Slide 9: Very Difficult and Expensive to Sample Large Bins and Silos

## Slide 10: Grain Cooling with Controlled Aeration
Computer controlled temperature monitoring and fan aeration system installed
Compared grain temperatures with summer aeration to no aeration

## Slide 11
July 21
Dec. 12
Average Grain Temperature in 8 Aerated vs 8 Non-aerated Bins
Fans turned on when air temperature fell below grain temperature.
91 F
57 F
36 F

## Slide 12: Registered Fumigants in the USA
Methyl Bromide
Phosphine
Sulfuryl Fluoride
Carbon Dioxide

## Slide 13: Challenges and Opportunities for Fumigation
Methyl Bromide being banned…
Phosphine resistance in grain insects…
Sulfuryl Fluoride; the learning curve…
Alternative fumigants…?..?..?..?
Residual chemicals in stored products
  Grain protectants
  Surface sprays
Biologically based controls

## Slide 14: Metallic Phosphide Salts: Most Common
Magnesium Phosphide
Mg3P2 + 6H2O  3Mg(OH) 2 + 2PH3
Aluminum Phosphide
AlP + 3H2O  Al(OH)3 + PH3

## Slide 15: Variables that Affect Fumigation Success
Species of target pest
Insects-Most tolerant life stage: egg, larva, pupa, adult
Gas concentration
Exposure time
Temperature

## Slide 16
%Kill from Increasing Doses
Probit Regression can Predict Dose Needed
LD99

## Slide 17: Dose-Mortality Results at 77oF
Chart: % Egg Mortality at 77oF
| 0 | 0 | 0 | 0 | 42.91 | 29.86 | 33.24 | 31.35 | 46.339999999999996 | 42.48 | 45.309999999999995 | 39.730000000000011 | 64.739999999999995 | 63.03 | 54.160000000000011 | 54.660000000000011 | 66.739999999999995 | 74.669999999999987 | 65.5 | 65.3 | 84.710000000000022 | 89.05 | 80.349999999999994 | 83.56
% Mortality | 6.7 | 0 | 3 | 3.4 | 87.3 | 56.8 | 54.1 | 44.4 | 85.7 | 65.7 | 71 | 83.3 | 100 | 95.3 | 94.3 | 97.4 | 100 | 100 | 100 | 97.5 | 100 | 100 | 100 | 100

## Slide 18: Dose-Mortality Results at 60oF
Chart: % Egg Mortality at 60oF
| 0 | 0 | 0 | 0 | 87.224999999999994 | 78.197000000000003 | 84.172999999999988 | 83.873999999999981 | 94.72 | 102.92 | 76.735000000000014 | 72.786000000000001 | 120.596 | 121.786 | 124.77800000000001 | 123.31699999999999 | 144.70299999999997 | 138.60900000000001 | 145.96300000000002 | 132.97999999999999 | 163.345 | 162.81 | 158.91499999999999 | 165.80600000000001 | 175.46600000000001 | 162.69800000000001 | 184.86600000000001 | 189.732 | 189.21099999999998 | 203.929 | 213.589 | 188.54900000000001
Mortality | 7 | 23.5 | 12.2 | 5.7 | 90.6 | 80.4 | 81.1 | 48.6 | 90 | 91.9 | 66 | 48.9 | 100 | 93.8 | 94.4 | 94.4 | 100 | 100 | 96.4 | 95.9 | 100 | 100 | 100 | 98.2 | 100 | 100 | 100 | 97.6 | 100 | 100 | 100 | 100

## Slide 19: Phosphine: Cheap, Easy and Effective
Gas is light-weight; penetrates well
Tablets/pellets are very economical
Effective for most pests
Corrosive to electrical fixtures
Some insects are resistant,….. and it’s spreading!

## Slide 20: Better Phosphine Fumigation
Seal bin very well
Monitor PH3 concentrations with proper equipment
Use higher concentration for much longer time at warm grain temperature: 1000+ ppm, 14 days, 80+ F
Use Phosphine from cylinders for better gas control

## Slide 21: Why are there Failures with Phosphine?
Leaks, leaks and leaks
Too few pellets or tablets
Grain too dry, too cool, or too hot
Poor distribution of gas
High amount of dockage
Bad treatment followed by emergence of survivors
Re-invasion of insects
Insects may be resistant

## Slide 22: Under-Roof Vents

## Slide 23: Sealing Under-Roof Vents

## Slide 24: Seal Aeration Fan Motors

## Slide 25: Seal Aeration Fan Transitions

## Slide 26: Seal Steel Bin Roof Eaves

## Slide 27: Seal Steel Bin Roof Eaves

## Slide 28: Cylinder-based Phosphine Gas
ECO2Fume – Approx. 2% Phosphine + 98% CO2
Vaporphos is >99% Phosphine gas rapidly diluted in air
No confined space entry for application
Will reach target concentration fast
Can add more gas as needed
More expensive than solid phosphides

## Slide 29
Phosphine Concentration in Bins

## Slide 30: ProFume® = Sulfuryl Fluoride for Food (same as Vikane ® for non-food structures)
DAS proposed SF as a MB alternative > 15 years ago
Stored gain registration was received first
Now fully registered in US, EU, AU and other countries
Can kill PH3-resistant insects; diff. mode of action
Limited by a maximum dose of 1500 CTP; also some insects hard to kill

## Slide 31: SF (ProFume) Loss from Sorption on Grains
Separate experiments done with wheat, corn and rough rice
All jars were held for 7 days; gas samples were taken frequently
Jars were exposed to one of three target concentrations in oz/mcf: 62.5, 31.3 and 15.6
All experiments were conducted at 20, 25 and 30 C
After 7 days each jar was opened, flushed with forced air for 30 seconds, then re-sealed to allow for desorption of SF from the grain.
Samples of air inside desorbing jars were taken at 1, 2, 4 and 24 hrs.

## Slide 32
Ham Mite: In Need of MB Alternative

## Slide 33: Mortality of Ham Mites under SF: 48h, 25oC
Above the EPA label rate

## Slide 34: ProFume + Heat for Mite Eggs!
Chart: Ham mite egg mortality (no hatch) after treatment with approx. 1400 g-hr/m3 ProFume at different temperatures
| 25 ºC Control | 25 ºC | 30 ºC | 35 ºC | 40 ºC
Mortality % | 3.3333 | 11.1111 | 12.2222 | 26.6667 | 100

## Slide 35: Potential limitations to SF
The 1500 CTP is a critical point before which treatment MUST STOP
Sone life stages/species are more tolerant to SF than others, especially at cool temps
Sorption by commodity can limit available gas for killing pests—but CTP applied still holds!
Must be skilled and experienced with SF for cost-effective applications

## Slide 36: Alternatives to Current Fumigants
Gases that could be registered by EPA
Controlled or modified atmospheric gases
Biologically-based controls
IPM – Integrated Pest Management

## Slide 37: Fumigants with Potential for Registration on Commodities and Structures
Ethyl Formate: food safe
Propylene Oxide, PPO: currently registered antimicrobial
MITC from Metam Sodium: registered soil fumigant
Metam Sodium
MITC, Methyl Isothiocyanate
Ethyl Formate
PPO

## Slide 38: Normal Atmosphere
Nitrogen, N2 = 78.0%
Oxygen, O2 = 20.9%
Carbon Dioxide, CO2 = 0.03%
Sea Level Pressure = 760 mm Hg

## Slide 39: Controlled Atmosphere: High CO2
High doses + good sealing + long exposures
Can be very expensive
Best for chamber fumigations, when other chemicals are not advised (museum artifacts)

## Slide 40: Mortality of Ham Beetles Under CO2
60% CO2 was needed to kill 100% ham beetle eggs and adults at 144h

## Slide 41: Use a Vacuum Pump to get 1% Oxygen
The “Cocoon” with organic cocoa under vacuum

## Slide 42: Biologically Based Controls
Diatomaceous earth: DE, death by desiccation
Bio-pesticide: Spinosad (Sensat®)
Insect Growth Regulators – IGRs
Extreme Temperatures—Heat and Cold

## Slide 43
Diatoms

## Slide 46: Biological Insecticide: Spinosad
A reduced-risk pesticide – low mammalian and avian toxicity
Derived from a bacterial fermentation product
Broad-spectrum – toxic by ingestion and contact
Extremely effective against lesser grain borer
Registered in U.S. at 1.0 ppm, Bayer has Sensat®…
May/will be approved for Organic Foods

## Slide 47: Small Bin Trial of Spinosad at Oklahoma State University
Replicated bin study
Spinosad alone at 1 ppm
Reldan alone at 6 ppm
Untreated bins
Grain stored 2 years with no other treatments

## Slide 48: Average No. of Insect-Damaged Kernels, IDK, per 100g Sample after Two Years (32+ IDK not for humans)
Untreated 130
Reldan 942
Spinosad 2

## Slide 49: What is an IGR?
IGR = Insect Growth Regulator
Chemical mimic of insect growth hormone
Does not kill adults or larvae directly
Insect dies when molting is disrupted
Extremely non-toxic and insect specific
Very safe for applicators and for food residues

## Slide 50: Effects of IGRs-Insects put on surface as larvae….
Developed on Untreated Surface
Developed on Treated Surface

## Slide 51: Effective Grain Protectants Possible Alternative of PH3 Resistant Pest ** Represent different AI ** ** Must apply while turning grain **
Spinosad (bacteria isolate; maybe not available)
Centynal (deltamethrin)
Storcide II (combination of deltamethrin + Reldan)
Diacon II (methoprene IGR)
Phantom (chlorfenapyr; labeled for surfaces)

## Slide 52: Summary and Conclusions
Methyl Bromide is now gone for domestic uses
Phosphine resistance is spreading in grain insects
Resistance management is needed to preserve phosphine
ProFume is a PH3 alternative. Good sealing, adequate exposure and warm temperatures are needed to kill tolerant life stages (eggs, pupae)
Grain managers will need to adjust their culture to use PH3 effectively and try various alternatives if needed
Adopt an IPM program with prevention and monitoring and then proper, effective fumigation as an action tool

## Slide 53: Thank You Very Much
Tom Phillips
785-532-4720
twp1@ksu.edu